## Slide 1
Design and Simulation of Half Adder and Full Adder Using Logisim
Digital Electronics / DDCA Mini Project

## Slide 2
1. Introduction
Adders are combinational digital circuits used to perform binary addition.
A Half Adder adds two 1-bit binary numbers.
A Full Adder adds three 1-bit inputs: A, B, and Carry-in.
Logisim is used to design, simulate, and verify the circuits.

## Slide 3
2. Objectives
Design a Half Adder using basic logic gates.
Design a Full Adder using basic logic gates.
Create and simulate both circuits in Logisim.
Verify the outputs using truth tables.
Understand Sum and Carry generation.

## Slide 4
3. Half Adder
Inputs: A and B
Outputs: Sum (S) and Carry (C)
Sum is produced using an XOR gate.
Carry is produced using an AND gate.
Equations: S = A ⊕ B and C = A · B

## Slide 5
4. Half Adder Truth Table
A B | Sum Carry
0 0 | 0 0
0 1 | 1 0
1 0 | 1 0
1 1 | 0 1

## Slide 6
5. Half Adder in Logisim
Place two input pins: A and B.
Add one XOR gate for the Sum output.
Add one AND gate for the Carry output.
Connect A and B to both gates.
Connect the outputs to two output pins or LEDs labeled Sum and Carry.
Toggle the inputs and verify all four truth-table cases.

## Slide 7
6. Full Adder
Inputs: A, B, and Carry-in (Cin)
Outputs: Sum (S) and Carry-out (Cout)
A Full Adder can be constructed using two Half Adders and one OR gate.
Equations: S = A ⊕ B ⊕ Cin
Cout = AB + Cin(A ⊕ B)

## Slide 8
7. Full Adder Truth Table
A B Cin | Sum Cout
0 0 0 | 0 0
0 0 1 | 1 0
0 1 0 | 1 0
0 1 1 | 0 1
1 0 0 | 1 0
1 0 1 | 0 1
1 1 0 | 0 1
1 1 1 | 1 1

## Slide 9
8. Full Adder in Logisim
Create three input pins: A, B, and Cin.
Use two XOR gates to generate the Sum.
Use two AND gates to generate carry terms.
Use one OR gate to generate Cout.
Connect the gates according to the Full Adder equations.
Test all eight input combinations in Logisim.

## Slide 10
9. Simulation and Verification
Logisim allows input switches to be toggled between 0 and 1.
The circuit outputs change immediately according to the applied inputs.
For the Half Adder, verify 4 input combinations.
For the Full Adder, verify 8 input combinations.
The simulated outputs should match the theoretical truth tables.

## Slide 11
10. Comparison
Half Adder: 2 inputs, 2 outputs, no Carry-in.
Full Adder: 3 inputs, 2 outputs, includes Carry-in.
Half Adder is simpler and is suitable for adding two single bits.
Full Adders are combined to build multi-bit binary adders.
Full Adder is therefore more useful for practical binary arithmetic.

## Slide 12
11. Applications
Binary addition in computers and processors.
Arithmetic Logic Units (ALUs).
Digital calculators.
Counters and digital signal-processing circuits.
Multi-bit ripple-carry and other adder architectures.

## Slide 13
12. Conclusion
Half Adder and Full Adder circuits were designed using logic gates.
Both circuits were simulated and tested using Logisim.
The simulation results agree with their truth tables.
The experiment demonstrates how basic gates can perform binary arithmetic.

## Slide 14
13. References
Logisim – Digital logic circuit simulation software.
Digital Electronics / DDCA classroom notes.
Standard Boolean algebra and combinational-circuit concepts.