## Slide 1
HALF ADDER & FULL ADDER
Digital Logic Design using Logisim
Half Adder | Full Adder | Truth Tables | Logisim Simulation
KLH-FED-2026-Section-2--Batch-8
github.com/Keerthan858/KLH-FED-2026-Section-2--Batch-

## Slide 2
TEAM
Group Members
2620030661
Ande Keerthan
2620030342
Pothuri Nagasai Anirudh Varma
2620030346
Chinthapalli Siri Chandana
2620030347
Saikam Nandhini
2
Half Adder & Full Adder Using Logisim

## Slide 3
1. What is a Binary Adder?
A combinational circuit that adds binary numbers.
SUM is the result bit; CARRY is the overflow.
A core building block of ALUs, CPUs and calculators.
Two common circuits: Half Adder and Full Adder.
2

## Slide 4
2. Half Adder
Adds two 1-bit binary inputs: A and B
Inputs: A, B
Outputs: Sum (S), Carry (C)
SUM is produced by XOR: S = A ⊕ B
CARRY is produced by AND: C = A · B
3

## Slide 5
3. Half Adder Truth Table
A | B | SUM (A⊕B) | CARRY (A·B)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
4

## Slide 6
4. Half Adder in Logisim
Build and test the circuit
Place two Input Pins (A, B).
Add an XOR gate (SUM) and an AND gate (CARRY).
Connect A and B to both gates.
Attach Output Pins/LEDs to SUM and CARRY.
Toggle inputs and check all 4 truth-table cases.
5

## Slide 7
5. Full Adder
Adds A, B and Carry-In (Cin)
Inputs: A, B, Cin
Outputs: SUM and Carry-Out (Cout)
SUM = A ⊕ B ⊕ Cin
Cout = AB + Cin(A ⊕ B)
Built from two Half Adders + one OR gate.
6

## Slide 8
6. Full Adder Truth Table
A | B | Cin | SUM | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
7

## Slide 9
7. Full Adder using Two Half Adders
Two Half Adders + one OR gate — modular, easy to build, test and expand
8

## Slide 10
8. Full Adder in Logisim
Recommended component layout
Inputs: A, B, Cin (3 Input Pins).
Create HA1 with XOR + AND.
Feed HA1 SUM into HA2 with Cin.
OR the two carry outputs to get Cout.
Two Output Pins/LEDs for SUM and Cout.
Test all 8 input combinations.
9

## Slide 11
9. Half Adder vs Full Adder
Feature | Half Adder | Full Adder
Inputs | 2 (A, B) | 3 (A, B, Cin)
Outputs | SUM, Carry | SUM, Cout
Carry-In | Not supported | Supported
Typical use | LSB/basic addition | Multi-bit binary addition
Expansion | Limited | Can be cascaded
10

## Slide 12
10. Key Takeaways
Half Adder = XOR + AND
Full Adder = two Half Adders + OR
Carry-In lets Full Adders chain for multi-bit addition.
Logisim makes gate-level design and testing easy.
Always test every input combination before trusting the circuit.
11

## Slide 13
THANK YOU
Questions?
Half Adder • Full Adder • Logisim
12